## Slide 1: Data Processing of Resting-State fMRI: DPARSF
严超赣
Chao-Gan Yan, Ph.D.
yancg@psych.ac.cn
http://rfmri.org/yan
Institute of Psychology, Chinese Academy of Sciences

## Slide 2: DPARSF
(Yan and Zang, 2010)

## Slide 3: Data Processing Assistant for Resting-State fMRI (DPARSF)
Yan and Zang, 2010. Front Syst Neurosci.
http://rfmri.org/DPARSF

## Slide 4: DPABI: a toolbox for Data Processing & Analysis of Brain Imaging
http://rfmri.org/dpabi
http://dpabi.org
License: GNU GPL
Chao-Gan Yan Programmer Initiator
Xin-Di Wang Programmer

## Slide 5: Resting State fMRI Data Processing
Preprocessing
FC (SCA)
ReHo
ALFF/fALFF
Degree
…
Statistical Analysis
Results Viewing

## Slide 6: Resting State fMRI Data Processing
Slice Timing
Realign
Normalize
Smooth
Detrend
ALFF/fALFF
FC (SCA)
ReHo
Degree
VMHC
…
Calculate in MNI Space: TRADITIONAL order
Filter
Nuisance Regression

## Slide 7: Resting State fMRI Data Processing
Slice Timing
Realign
Nuisance Regression
Normalize
Smooth
ALFF/fALFF
FC (SCA)
ReHo
Degree
VMHC
…
Calculate in MNI Space: alternative order
Filter

## Slide 8: Resting State fMRI Data Processing
Slice Timing
Realign
Nuisance Regression
ALFF/fALFF
Filter
FC (SCA)
ReHo
Degree
…
Calculate in Original Space
Normalize
Smooth

## Slide 9: Resting State fMRI Data Processing
Template Parameters
9

## Slide 10: Data Organization
ProcessingDemoData.zip
  FunRaw
    Sub_001
    Sub_002
    Sub_003
  T1Raw
    Sub_001
    Sub_002
    Sub_003
Functional DICOM data
Structural DICOM data
http://rfmri.org/DemoData

## Slide 11: Data Organization
ProcessingDemoData.zip
  FunImg
    Sub_001
    Sub_002
    Sub_003
  T1Img
    Sub_001
    Sub_002
    Sub_003
Functional NIfTI data (.nii.gz., .nii or .img)
Structural NIfTI data (.nii.gz., .nii or .img)

## Slide 13
IMA
dcm
none

## Slide 14: Data preparation
Arrange each subject's fMRI DICOM images in one directory, and then put them in "FunRaw" directory under the working directory.
Subject 1’s DICOM files
FunRaw directory, please name as this
Subject 1’s directory
Working directory

## Slide 15: Data preparation
Arrange each subject's T1 DICOM images in one directory, and then put them in “T1Raw" directory under the working directory.
Subject 1’s DICOM files
T1Raw directory, please name as this
Subject 1’s directory
Working directory

## Slide 16: Preprocessing and R-fMRI measures Calculation
Working Dir where stored Starting Directory (e.g., FunRaw)
Detected participants
16

## Slide 17: Preprocessing and R-fMRI measures Calculation
Detected participants
17

## Slide 18: Preprocessing and R-fMRI measures Calculation
Number of time points
(if 0, detect automatically)
TR
(if 0, detect from NIfTI header)
Template Parameters
DICOM to NIfTI, based on MRIcroN’s
dcm2nii
Apply reorientation
matrices
18

## Slide 19
19

## Slide 20: Preprocessing and R-fMRI measures Calculation
Apply reorientation matrices:
  ReorientMats
  Rename to:
  DownloadedReorientMats

## Slide 21: Preprocessing and R-fMRI measures Calculation
Remove several first time points
Slice Timing
21

## Slide 22: Slice Timing
Why?
Huettel et al., 2004

## Slide 23: Preprocessing and R-fMRI measures Calculation
23
Total slice number
(if 0, The slice order is then assumed as interleaved scanning: [1:2:SliceNumber,2:2:SliceNumber]. The reference slice is set to the slice acquired at the middle time point, i.e., SliceOrder(ceil(SliceNumber/2)). SHOULD BE CAUTIOUS!!!)
Reference slice: slice acquired in the middle time of each TR
Slice order: 1:2:33,2:2:32 (interleaved scanning)
Realign

## Slide 24: Realign
Why?

## Slide 25: Realign
Check head motion:
{WorkingDir}\RealignParameter\Sub_xxx:
rp_*.txt: realign parameters
FD_Power_*.txt: Frame-wise Displacement (Power et al., 2012)
FD_VanDijk_*.txt: Relative Displacement (Van Dijk et al., 2012)
FD_Jenkinson_*.txt: Relative RMS (Jenkinson et al., 2002)

## Slide 26: Realign
(Yan et al.,
Neuroimage
2013)
26

## Slide 27: Realign
Check head motion:
{WorkingDir}\RealignParameter:
ExcludeSubjectsAccordingToMaxHeadMotion.txt
Excluding Criteria: 2.5mm and 2.5 degree in max head motion
None
Excluding Criteria: 2.0mm and 2.0 degree in max head motion
Sub_013
Excluding Criteria: 1.5mm and 1.5 degree in max head motion
Sub_013
Excluding Criteria: 1.0mm and 1.0 degree in max head motion
Sub_007
Sub_012
Sub_013
Sub_017
Sub_018
27

## Slide 28: Realign
Check head motion:
HeadMotion.csv: head motion characteristics for each subject (e.g., max or mean motion, mean FD, # or % of FD>0.2)
Threshold:
Group mean (mean FD) + 2 * Group SD (mean FD)
Yan et al., in press Neuroimage; Di Martino, in press, Mol Psychiatry
28

## Slide 29: Preprocessing and R-fMRI measures Calculation
29
Voxel-Specific Head Motion Calculation
(Yan et al.,
Neuroimage
2013)

## Slide 30: Voxel-Specific Head Motion Calculation
{WorkingDir}\VoxelSpecificHeadMotion\Sub_xxx:
HMvox_x_*.nii: voxel specific translation in x axis
FDvox_*.nii: Frame-wise Displacement (relative to the previous time point) for each voxel
TDvox_*.nii: Total Displacement (relative to the reference time point) for each voxel
MeanFDvox.nii: temporal mean of FDvox for each voxel
MeanTDvox.nii: temporal mean of TDvox for each voxel

## Slide 31: Preprocessing and R-fMRI measures Calculation
Reorient Interactively
This step could improve the accuracy in coregistration, segmentation and normalization, especially when images had a bad initial orientation.
Also can take as a QC step.

## Slide 32
32

## Slide 33
33

## Slide 34
34
Display the mean image after realignment. (Could take this step as a QC procedure.)
The reorientation effects on and realigned functional images and voxel-specific head motion images.
QC scores and comments are stored at {WorkDir}/QC

## Slide 35: Automask generation
35
For checking EPI coverage and generating group mask
FunImgAR/Sub_001
Masks/AutoMasks/

## Slide 36: Preprocessing and R-fMRI measures Calculation
36
T1 DICOM files to NIfTI (based on MRIcroN’s
dcm2nii)
Reorient T1 image Interactively
Crop T1 image (.nii, .nii.gz, .img)
(based on MRIcroN’s
Dcm2nii)

## Slide 37: Brain extraction (Skullstrip)
For Linux and Mac: Need to install FSL.
For Windows:
Thanks to Chris Rorden's compiled version of bet in MRIcroN, our modified version can work on NIfTI images directly.
37
For better coregistration

## Slide 38
38
T1Img/Sub_001
T1ImgBet/Sub_001
RealignParameter/Sub_001/mean*.nii
RealignParameter/Sub_001/Bet_mean*.nii
bet
Coregister
Apply
T1ImgCoreg/Sub_001
Segment
Bet & Coregistration

## Slide 39: Preprocessing and R-fMRI measures Calculation
Coregister T1 image to functional space

## Slide 40: Preprocessing and R-fMRI measures Calculation
40
Unified Segmentation.
Information will be used in spatial normalization.
(In SPM12: old segment)
Affine regularisation in segmentation
New Segment and DARTEL.
Information will be used in spatial normalization.

## Slide 41: By-Product: VBM
GM in original space
WM in original space
GM in normalized space
Modulated GM in normalized space
CSF in original space

## Slide 42: Preprocessing and R-fMRI measures Calculation
42
Nuisance Covariates Regression
Polynomial trends as regressors:
0: constant (no trends)
1: constant + linear trend (same as linear detrend)
2: constant + linear trend + quadratic trend
3: constant + linear trend + quadratic trend + cubic trend
...

## Slide 43: Preprocessing and R-fMRI measures Calculation
43
Head Motion regression model
Derivative 12: 6 head motion parameters, 6 first derivatives
6 head motion parameters
Friston 24-parameter model: 6 head motion parameters, 6 head motion parameters one time point before, and the 12 corresponding squared items (Friston et al., 1996).

## Slide 44: Preprocessing and R-fMRI measures Calculation
44
Voxel-specific 12-parameter model: the 3 voxel-specific translation motion parameters in x, y, z, the same 3 parameters for one time point before, and the 6 corresponding squared items
Head Motion Scrubbing Regressors

## Slide 45
Each “bad” time point defined by FD will be used as a separate regressor.

## Slide 46
Yan et al., 2013, Neuroimage

## Slide 47: Preprocessing and R-fMRI measures Calculation
Nuisance Regressors
(WM, CSF, Global)

## Slide 48: Nuisance Regression
48
Mask based on segmentation or SPM apriori
CompCor or mean [note: for CompCor, detrend (demean) and variance normalization will be applied before PCA, according to Behzadi et al., 2007]
Global Signal based on Automask

## Slide 49: Preprocessing and R-fMRI measures Calculation
Define other covariates

## Slide 50: Preprocessing and R-fMRI measures Calculation
50
Filtering
The filtering parameters will be used later (Blue checkbox).

## Slide 51: Preprocessing and R-fMRI measures Calculation
Spatial Normalization

## Slide 52: Normalize
Huettel et al.,
2004

## Slide 53: Normalize
Methods:
I. Normalize by using EPI templates
II. Normalize by using T1 image unified segmentation
III. Normalize by using DARTEL
IV. Normalize by using T1 templates (hidden)

## Slide 54: Normalize
III. Normalize by using DARTEL
Structural image was coregistered to the mean functional image after motion correction
The transformed structural image was then segmented into gray matter, white matter, cerebrospinal fluid by using a unified segmentation algorithm (New Segment)
DARTEL: create template
DARTEL: Normalize to MNI space. The motion corrected functional volumes were spatially normalized to the MNI space using the normalization parameters estimated in DARTEL.

## Slide 55: Preprocessing and R-fMRI measures Calculation
Smooth
For ReHo, Degree Centrality: don’t smooth before calculation
FWHM kernel settings can be applied to later steps

## Slide 56: Smooth
Why?
Reduce the effects of bad normalization
Increase SNR
…

## Slide 57
57
Mask
Default mask: SPM5 apriori mask (brainmask.nii) thresholded at 50%.
User-defined mask
Warp the masks into individual space by the information of DARTEL or unified segmentation.

## Slide 58: Preprocessing and R-fMRI measures Calculation
58
Linear detrend
(NO need since included in nuisance covariate regression)

## Slide 59: Preprocessing and R-fMRI measures Calculation
59
Nuisance Covariates Regression
If needed, then use the parameters set in the upper section.

## Slide 60: Preprocessing and R-fMRI measures Calculation
60
ALFF and fALFF calculation
(Zang et al., 2007; Zou et al., 2008)

## Slide 61: ALFF/fALFF
Zang et al., 2007; Zou et al., 2008
PCC: posterior cingulate cortex
SC: suprasellar cistern
Amplitude of low frequency fluctuation / Fractional ALFF
61

## Slide 62: Preprocessing and R-fMRI measures Calculation
62
Filtering
Use the parameters set in the blue edit boxes.

## Slide 63: Preprocessing and R-fMRI measures Calculation
63
Scrubbing

## Slide 64
The “bad” time points defined by FD_Power (Power et al., 2012) will be interpolated or deleted as the specified method.

## Slide 65: Preprocessing and R-fMRI measures Calculation
65
Regional Homogeneity (ReHo) Calculation
(Zang et al., 2004)

## Slide 66: ReHo (Regional Homogeneity)
Zang et al., 2004
Zang YF, Jiang TZ, Lu YL, He Y, Tian LX (2004) Regional homogeneity approach to fMRI data analysis. Neuroimage 22: 394–400.

## Slide 67: Preprocessing and R-fMRI measures Calculation
67
Regional Homogeneity (ReHo) Calculation
(Zang et al., 2004)

## Slide 68: Preprocessing and R-fMRI measures Calculation
68
Degree Centrality Calculation
(Buckner et al., 2009; Zuo et al, 2012)
> r Threshold
(default 0.25)

## Slide 69
Zuo et al., 2012

## Slide 70: Preprocessing and R-fMRI measures Calculation
Extract ROI time courses (also for ROI-wise Functional Connectivity)
70
Functional Connectivity (voxel-wise seed based correlation analysis)
Define ROI

## Slide 71: Define ROI
Dosenbach et al., 2010
71
Multiple labels in mask file: each label is considered as one ROI
Define other ROIs
Andrews-Hanna et al., 2010
Craddock et al., 2011

## Slide 74: Preprocessing and R-fMRI measures Calculation
74
Define ROI Interactively

## Slide 75
75
0 means define ROI Radius for each ROI seperately

## Slide 76
76

## Slide 77: Functional Connectivity
You will get the Voxel-wise functional connectivity results of each ROI in {working directory}\Results\FC:
zROI1FCMap_Sub_001.img
zROI2FCMap_Sub_001.img
For ROI-wise results, please see {working directory}\Results\FunImgARCW*_ROISignals.

## Slide 78: Preprocessing and R-fMRI measures Calculation
78
Voxel-mirrored homotopic connectivity (VMHC) (Zuo et al., 2010)
Prepare for VMHC: Further register to a symmetric template

## Slide 79: Preprocessing and R-fMRI measures Calculation
79
Voxel-mirrored homotopic connectivity (VMHC) (Zuo et al., 2010)

## Slide 80: VMHC
80
1) Get the T1 images in MNI space (e.g., wco*.img or wco*.nii under T1ImgNewSegment or T1ImgSegment) for each subject, and then create a mean T1 image template (averaged across all the subjects).
2) Create a symmetric T1 template by averaging the mean T1 template (created in Step 1) with it's flipped version (flipped over x axis).
3) Normalize the T1 image in MNI space (e.g., wco*.img or wco*.nii under T1ImgNewSegment or T1ImgSegment) for each subject to the symmetric T1 template (created in Step 2), and apply the transformations to the functional data (which have been normalized to MNI space beforehand). Please see a reference from Zuo et al., 2010.

## Slide 81
81
Gee et al., 2011
Zuo et al., 2010

## Slide 82: Preprocessing and R-fMRI measures Calculation
82
Parallel Workers (if parallel computing toolbox is installed)
Each subject is distributed into a different worker. (Except DARTEL-Create Template)

## Slide 83: Preprocessing and R-fMRI measures Calculation
83
Multiple functional sessions
1st session: FunRaw
2nd session: S2_FunRaw
3rd session: S3_FunRaw
…

## Slide 84
84
Starting Directory Name
If you do not start with raw DICOM images, you need to specify the Starting Directory Name.
E.g. "FunImgARW" means you start with images which have been slice timed, realigned and normalized.
Abbreviations:
A - Slice Timing
R - Realign
W - Normalize
S - Smooth
D - Detrend
F - Filter
C - Covariates Removed
B - ScruBBing

## Slide 85: Preprocessing and R-fMRI measures Calculation
85
Connectome-wide association studies based on multivariate distance matrix regression (Shehzad et al., 2014)
Resource consuming as compared to other measures

## Slide 86
86
Shehzad et al., 2014. Neuroimage

## Slide 87: Resting State fMRI Data Processing
Template Parameters
87

## Slide 88: Resting State fMRI Data Processing
Calculate in MNI space
88
Calculate in Original space

## Slide 89: Preprocessing and R-fMRI measures Calculation
89
Normalize measures (derivatives) calculated in original space into MNI space
Use the parameters set in the upper section.

## Slide 90: Preprocessing and R-fMRI measures Calculation
90
Smooth R-fMRI measures (derivatives)
Use the parameters set in the upper section.

## Slide 91: Preprocessing and R-fMRI measures Calculation
91
Warp masks into original space

## Slide 92: Resting State fMRI Data Processing
Intraoperative Processing
92

## Slide 93: Preprocessing and R-fMRI measures Calculation
93
No realign since there is no head motion. DPARSFA will generate the mean functional images automatically.
Define ROI Interactively

## Slide 94: Resting State fMRI Data Processing
VBM
94

## Slide 95: VBM
95
Only New Segment + DARTEL is checked
Define the Starting Directory Name as T1Raw

## Slide 96: Resting State fMRI Data Processing
Blank
96

## Slide 97: Blank
97

## Slide 98: Save and Load Parameters
Save parameters to *.mat
Load parameters from *.mat

## Slide 99: Further Help
99
Further questions:
http://rfmri.org/dpabi
The R-fMRI Network

## Slide 100: Further Help
100

## Slide 101
101

## Slide 102
102

## Slide 103
103
Send emails only to rfmri.org@gmail.com: 1) sending new email means you are posting your personal blogs, 2) replying email means you are posting comments to that topic/blog, 3) then all the other R-fMRI nodes will receive email updates of your posts.

## Slide 104
104

## Slide 105: The R-fMRI Maps Project
105

## Slide 106
招贤纳士
博士研究生1名
硕士研究生1名
助理研究员2名
博士后1名

## Slide 107: Acknowledgments
Funding
National Natural Science Foundation of China
Chinese Academy of Sciences
Child Mind Institute
Michael P. Milham
NYU Child Study Center
F. Xavier Castellanos
Chinese Academy of Sciences Xi-Nian Zuo
Hangzhou Normal University Yu-Feng Zang
Beijing Normal University
Yong He
Xin-Di Wang
Peking University
Jia-Hong Gao
Wei-Wei Men
Notes: Different Axis!!!

## Slide 108: Thanks for your attention!
108